## Slide 1
Group 8
B06901071 何承叡
B06901058 陳聖佑
MIPS Final Project Presentation

## Slide 2: Outline
Baseline -- result & optimization
Branch prediction -- result & analysis
L2 cache -- result & analysis
MultDiv -- result

## Slide 3: Baseline
1
Result & Optimization

## Slide 4: Baseline
Cycle Time: 2.9ns
AT value (hasHazard, problem size = 16) : 1,843,105,994.65
Critical path
pc
…
IF
ID
WB
IF/ID
ID/EX
MEM/WB
=
forward
control

## Slide 5: Baseline
pc
…
IF
ID
WB
IF/ID
ID/EX
MEM/WB
=
forward
control
Cycle Time: 2.9ns
AT value (hasHazard, problem size = 16) : 1,843,105,994.65
Critical path

## Slide 6: Baseline Optimization
Cycle Time: 2.5ns
AT value (hasHazard, problem size = 16) : 1,790,037,417.36
If branch is taken, the penalty will be two stall cycle
pc
…
IF
ID
WB
IF/ID
ID/EX
MEM/WB
=
forward
control
branch address

## Slide 7: Branch Prediction
2
Analysis & Optimization

## Slide 8: 2-bit Branch Prediction
Methdology
Taken2
Taken1
NotTaken2
NotTaken1
correct
wrong
correct
wrong
wrong
correct
wrong
correct

## Slide 9: 2-bit Branch Prediction
Cost Cycle Difference (No Branch Prediction – 2-bit Branch Prediction)
  Never branch: 0
  Interleave branch: -3
  Always branch: 9998
No Branch Prediction
2-bit Branch Prediction
(nb_notBr, nb_interBr, nb_Br) = (10000, 10000, 10000)

## Slide 10: Branch Prediction with Local History Table
Methdology
N=2
  When branch pattern is 1010…
    => 1
    01 => 0
Branch History
0010
.
.
.
History Table
N bit
To Do

## Slide 11: Branch Prediction with Local History Table
Cost Cycle Difference (No Branch Prediction – 2-bit Branch Prediction)
  Never branch: 0
  Interleave branch: 9995
  Always branch: 9997
No Branch Prediction
2-bit Branch Prediction
with Local History Table
(nb_notBr, nb_interBr, nb_Br) = (10000, 10000, 10000)

## Slide 12: Cost Cycle Comparison
 | hasHazard | I_mem_BrPred |  |  | 
 | Problem Size = 47 | Never Branch | Interleave Branch | Always Branch | Total
No Branch Prediction | 16466 | 50040 | 70016 | 40021 | 160077
1-bit | 16491 | 50040 | 70007 | 30023 | 150070
2-bit | 17458 | 50040 | 70019 | 30023 | 150082
History Table | 15352 | 50040 | 60021 | 30024 | 140085
(nb_notBr, nb_interBr, nb_Br) = (10000, 10000, 10000)

## Slide 13: Branch Prediction Gate Level
Cycle Time: 2.8ns
Area of BPU: 14,045.985096
AT value (hasHazard, problem size = 16)
  1,765,753,263.08

## Slide 14: L2 Cache
3
Result & Analysis

## Slide 15: L2 Cache
Separate
32blocks & 4 words
MP1=MP2=8cycles, HT2=2cycles
 | I cache | D cache
MR1 | 0.04% | 10%
MR2 | 80% | 1.7%
CPI(original) | 1.003 | 1.8
CPI(+L2cache) | 1.003 | 1.214
improvement | 0% | -32%

## Slide 16: Multiply&Divide
4
Result

## Slide 17: Multiplication & Division
Methdology
multiply
divide

## Slide 18: Multiplication & Division
Cycle Time: 2.8ns
Total Execution Time: 2,991.8
Area of MultDiv: 22,838.516852
AT value (MultDiv, problem size = 12)
  955,031,738.987

## Slide 19: Thanks for Your Listening